## Slide 1
ECE4078 Intelligent robotics
Lab 3-1: Training a Fruit&Veg Detector
AI art generated by https://www.craiyon.com/
(prompt: “a penguin robot shopping for fruits and vegetables in a supermarket”)

## Slide 2
ECE4078 Intelligent robotics
Week | Objectives | Milestones
2: M1-1 | Introduction and setup | 
3: M2-1 | Calibration, ARUCO markers | M1 due
4: M2-2 | SLAM | 
5: M2-3 | SLAM | 
6: M3-1 | Object recognition & localisation | M2 due
7: M3-2 | Object recognition & localisation | 
8: M4-1 | Navigation & Planning | M3 due
9: M4-2 | Navigation & Planning | 
10: M5-1 | Integration | M4 due
11: Final | Improvement | M5 due
12: Final | Final demo & competition | Final demo
*

## Slide 3
Milestone 3
Your PenguinPi can map the supermarket aisles and itself after M2, but how does it find the fruits and vegs to shop for? In M3, you’ll focus on object recognition and localization using machine learning.
There are 8 types of fruits and vegs selling at the supermarket, and a total of 10 objects in an arena in addition to the 10 ARUCO markers (there may be duplicates or missing target types):
lime orange lemon tomato garlic potato capsicum pumpkin

## Slide 4
M3: Overview
Task 1: collecting a dataset of target fruits and vegs (Week 6)
Task 2: Training a YOLO model for object detection and segmentation (Week 6)
Task 3: Estimating object poses (Week 7)
Live demo marking of M3 in Week 8: detector performance + object pose estimation performance
Note: for M3 we DO NOT recommend developing your detector in the simulator, as an object detector trained in the simulator is likely to have significantly worse performance when applied in real world.
You can still use the simulator to develop the target pose estimation part (Week 7), but you’ll need to train two detectors, one for the real world, one for the simulator.

## Slide 5
M3: collecting data (wk6)
Task 1: collecting a dataset of target fruits and vegs (Week 6)
Do these during the lab session:
Take photos of each target object using PenguinPi’s camera (operate.py allows you to drive the robot around, press “i” to save an image) from various angles and under various lighting conditions, use a simple background (e.g., a white paper) for easy background randomisation later
Measure the dimensions of each target object (in meters), which you’ll need for estimating their location in wk7 (update target_dimensions_dict in TargetPoseEst.py)

## Slide 6
M3: collecting data (wk6)
Developing a training dataset using photos you take (can be done outside of the lab)
Step 1.1: remove background in the photos you took (use this tool or anything else you prefer)
Step 1.2: add random background (see image_background_randomiser), you can add other variances to increase diversity in the training dataset, such as object orientations or sizes

## Slide 7
M3: collecting data (wk6)
Developing a training dataset using photos you take (can be done outside of the lab)
Step 1.3: annotate your dataset
We recommend Roboflow as it’s free and the annotation can be exported in YOLO training format. There is also an assisted labelling feature to help speed things up
Make sure your bounding boxes are tight around the object, as the bounding box size is used for target pose estimation

## Slide 8
M3: collecting data (wk6)
Developing a training dataset using photos you take (can be done outside of the lab)
Step 1.4: generating the dataset in YOLO format (Roboflow)
You can use the image augmentation options of Roboflow to increase diversity in the dataset

## Slide 9
M3: Training YOLO (wk6)
Task 2: Training the network (Week 6)
YOLO: “You Only Look Once”, one the most popular image segmentation and classification model
Install YOLOv8: python -m pip install ultralytics
Please follow YOLOv8_training_notebook.ipynb for training YOLO with your collected dataset
You can train your model using Google Colab or on your local machine (don’t train it inside the VM)

## Slide 10
M3: Training YOLO (wk6)
Example YOLO detector
(can only recognize garlic, orange, pumpkin)
Hints:
Tuning confidence threshold: any bounding box above this threshold is considered valid
Add a wide range and aggressive amounts of noise / distortion to your training images so that it can handle potential lighting conditions and disturbances in the real world

## Slide 11
M3: Estimating Object Location (wk7)
Task 3: Estimating object poses (Week 7)
Given YOLO’s bounding boxes, true dimensions of the objects, and the robot’s pose (estimated by SLAM) at the time of observation, calculate the X-Y coordinates of the object in the arena
You will modify “TargetPoseEst.py”
M3 evaluation: live demo marking in Week 8
Will talk more about these next week

## Slide 12
M2 marking
Please check GitHub for the marking procedure. M2 is marked as a group assignment.
You have a total of 15 minutes for setup, demonstration and submission.
There are two marking arenas running M2 marking in parallel. The groups will be marked in random order in one of the two marking arenas.
Don’t come to the marking arena unless it’s your group’s turn.
You can perform as many runs as you like as long as you can finish within the time limit. Each run has a max of 3 allowed collisions.
Remember to rename the maps so the later runs don’t overwrite your earlier runs.
We’ll mark all the generated SLAM maps you submit and take the best result for your M2 mark:
slam_score = ((0.12 - Aligned_RMSE)/(0.12 - 0.02)) x 80 (0 ≤ slam_score ≤ 80)
Total M2 mark = slam_score + (NumberOfFoundMarkers x 2) - (NumberOfCollidedMarkers x 5)